## Slide 1: ARM Cortex A8 Pipeline
EE126 Wei Wang

## Slide 2
Cortex A8 is a processor core designed by ARM Holdings.
Application: Apple A4, Samsung Exynos 3110.
What’s the pipeline architecture in Cortex A8?
Deeper pipeline and superscalar pipeline.

## Slide 3
Deeper Pipeline
For pipeline, the speed is limited by the length of the longest stage, and the longest stage is set to be the standard one cycle time. For the deeper pipeline, the time of the new sub-stage is small. The smaller time resolution therefore leads to less time to complete one instruction.
Why does it break one cycle into several cycles?

## Slide 4
Superscalar Pipeline
It is a form of instruction level parallelism, which is faster than normal pipeline.

## Slide 5
Cortex A8 Pipeline Main Architecture:

## Slide 6
Execution stages: 6 stage pipeline.
It can extensively support of key forwarding path. Result data is from the outputs of shift, ALU and MUL immediately as it is produced. The intermediate execution stage results can be forwarded. Unlike the simple pipeline, only the final execution stage result can be forwarded.
Two symmetric ALU pipeline, a multiple pipeline and an address generator for load and store.
1. For the ALU pipeline:
E0 access register file;
E1 shift if needed;
E2 ALU function;
E3 complete saturation if needed;
E4 change in control flow;
E5 write back to register file.
2. For the Mul pipeline:
E1-E3 implement multiply;
E4 perform addition.;
E5 write back.

## Slide 7
Deep pipeline and superscalar pipeline have good performance. Why not increases the sub-stages and the parallel instructions?
What’s the limitations?

## Slide 8
Data Dependency
Solution: Stall the adder until the multiplier has finished.

## Slide 9
Output dependency:
An output dependency occurs if two paralleled instructions are writing into the same location. An error occurs if the second instruction implement before the first one.

## Slide 10
Antidependency:
An antidependency exists if an instruction uses a location as an operand while a following one is writing into that location; if the first one is still using the location when the second one writes into it, an error occurs.

## Slide 11
Solution for the output independency and antidependency: Use other register.
Alternative ways to handle dependency:
Compiler will generate instructions with less dependency.

## Slide 12
Summary: Cortex architecture is a high speed architecture by using deeper pipeline and superscalar pipeline.

## Slide 13: Thank you