## Slide 1: Multiprocessor network topologies
EE 126 Computer Engineering
Final Project
Fanying Ye

## Slide 2: Contents
Introduction
Overview
Comparison of common approaches
The future trends
Conclusions

## Slide 3: Introduction
Image processing
Weather computation
http://www.kitware.com/blog/files/128_579534278.jpg
http://blogs.siam.org/wp-content/uploads/sites/2/2014/01/bunge2web.jpg

## Slide 4: Introduction
Scalability
Communication efficiency
Power consumption
Problems:
Shared medium arbitrated bus[1]

## Slide 5: Introduction
New concept:
Network on chip
(NoC)[2]

## Slide 6: Network topology
The organization of the shared router nodes and channels in an on-chip network[1]

## Slide 7: Principal:
Power consumption
Area
Throughput

## Slide 8: Overview
Classification

## Slide 9: 2D mesh in CLICHE
Most common among all interconnection topologies
It allows incorporation of large number of IP cores in a regular-shape structure [1][2]

## Slide 10: Intel’s Teraflops Research Chip
Network on a chip – In addition to the compute element, each core contains a 5-port message passing router.
These are connected in a 2D mesh network that implement message-passing.

## Slide 11: 2D torus
The switches at the edges are linked to the switches at the opposite edge through folded channels
The long end-around connections can generate excessive delays [1][3]

## Slide 12: 2D folded torus
Excessive delay in torus can be avoided by folding the torus
It renders a more suitable VLSI implementation [1][3]

## Slide 13: Octagon
It is designed to overcome the scalability problem as every node can expand into an octagon [1]

## Slide 14: Binary Tree
Each router node is linked to 2 nodes in the subsequent level
The main problem : the single parent node especially the root can easily become traffic bottlenecks [3]

## Slide 15: Fat tree in SPIN
Fat tree: a node can have more than one parent. This model can alleviate the problem in binary tree.
Every node has four children and the parent is replicated four times at any level of the tree. [1][3]

## Slide 16: BFT-Butterfly Fat-Tree
Each router node is linked to either 4 routers or resource nodes. [1][2]

## Slide 17: Comparison of Throughput
BFT, CLICHE, and Folded Torus provide a lower throughput than do SPIN and Octagon [1]

## Slide 18: Comparison of Area Overhead
SPIN and Octagon have a considerably higher silicon area overhead. [1]

## Slide 19: Comparison of Energy dissipation
SPIN and Octagon have greater average energy dissipation at saturation than the others [1]
For uniform
traffic
For localized
traffic

## Slide 20: Advantages and Disadvantages
 | Advantages | Disadvantages
SPIN | High throughput Good scalability | 1.High silicon area overhead 2. Greater average energy dissipation 3. Wiring complexity
2D-Mesh | Simple architecture with good scalability | Low throughput
2D-Torus | low power consumption | Excessive delay
Folded Torus | Low power consumption Small delay | High silicon area overhead
Octagon | High throughput | 1.High silicon area overhead 2. Greater average energy dissipation
BFT | Great Localization | Wiring complexity

## Slide 21: Future trend
3D-ICs can achieve better performances, more flexibility, and higher throughput . [5]
Combining the NoC structure with the benefits of the 3D integration lead us to present 3D-NoC as a new architecture.[6]
3D-topology
[7]
[8]

## Slide 22: Conclusion
NoC is an efficient on-chip communication architecture for SoC architectures. Topologies is a key factor in MP-NoC design.
Some architectures can sustain very high data rates at the expense of high-energy dissipation and considerable silicon area overhead, while others can provide a lower data rate and lower energy dissipation levels.
With increasing number of processors in MP-SoC, the 3D topology will be the next hotspot in research.

## Slide 23: References
[1] Pratim Pande, Cristian Grecu, Michael Jones, Andre ́ Ivanov and Resve Saleh, “Networks on Chips: A New SoC ParadigmPerformance Evaluation and Design Trade-Offs for Network-on-Chip Interconnect Architectures ,” IEEE TRANSACTIONS ON COMPUTERS, VOL. 54, NO. 8, AUGUST 2005
[2] T. Bjerregaard and S. Mahadevan, “A survey of Research and Practice of Network-on-Chip”, ACM Computing Surveys, Vol. 38, March 2006.
[3] Tetala Neel Kamal Reddy, Ayas Kanta Swain, Jayant Kumar Singh and Kamala Kanta Mahapatra, “PERFORMANCE ASSESSMENT OF DIFFERENT NETWORK-ON-CHIP TOPOLOGIES ”, 2014 2nd International Conference on Devices, Circuits and Systems (ICDCS)
[4] http://download.intel.com/pressroom/kits/Teraflops/Teraflops_Research_Chip_Overview.pdf
[5] César Marcon, Ramon Fernandes, Rodrigo Cataldo, Fernando Grando, Thais Webber, Ana Benso, Letícia B. Poehls, “Tiny NoC: A 3D Mesh Topology with Router Channel Optimization for Area and Latency Minimization”, 2014 27th International Conference on VLSI Design and 2014 13th International Conference on Embedded System
[6] K. Banerjee, S. J. Souri, P. Kapur, and K. C. Saraswat, “3-D ICs: A Novel Chip Design for Improving Deep-Submicrometer Interconnect Performance and Systems-on-Chip Integration,” Proceedings of the IEEE, Vol. 89, No. 5,pp. 602-633, May 2001.
[7] Avik Bose, Prasun Ghosal, Saraju P. Mohanty, “A Low Latency Scalable 3D NoC Using BFT Topology with Table Based Uniform Routing ”,2014 IEEE Computer Society Annual Symposium on VLSI , pp136
[8]Y.-L. Jeang et al. “Mesh-Tree Architecture for Network-on-Chip Design”. International Conference on Innovative Computing, Information and Control (ICICIC), pp.1-4.2007.